## Slide 1
BHOPAL IMPACT LAB 2026 · TRACK 2: VISARJAN GHAT WATCH
Visarjan Ghat Watch (विसर्जन घाट वॉच)
Turning 3 Years of Buried MPPCB Water Tests into an Auditable Action Plan for Bhopal 2026
Team: NeerRakshak | Lead: Anoop Shukla (anoopshuklanew00@gmail.com)
Target Decision: BMC Resource Allocation for Durga Visarjan (20 October 2026 — 9 Days Remaining)

## Slide 2
BHOPAL IMPACT LAB 2026 · TRACK 2
The Crisis Behind Bhopal's Immersion Ghats
4 Anoxic Events (0.0 mg/l DO)
Dissolved Oxygen hit 0 mg/l four times at Bairagarh Kund across 2023-2025. Water at zero oxygen supports no fish life.
89.3% Organic BOD Failure
100 of 112 Biochemical Oxygen Demand readings exceed statutory limits (<= 3.0 mg/l). Median BOD is 6.4 mg/l (Peak: 22.0 mg/l).
36.2% Oxygen Depletion
42 of 116 Dissolved Oxygen tests fail CPCB Class B outdoor bathing criteria (>= 5.0 mg/l), creating acute ecological dead-zones.
9 Days to Durga Visarjan
NGT has banned immersion in Upper/Lower lakes. On 20 Oct 2026, BMC officers must allocate aeration, skimmers & bunds without guesswork.

## Slide 3
BHOPAL IMPACT LAB 2026 · TRACK 2
Visarjan Ghat Watch: Evidence-Based Decision Support
1. Multi-Criteria Risk Scoring (MCDA)
Combines DO deficit, BOD organic spike, and pH deviation into a normalized 0-100 composite risk score, ranking all 7 ghats from Critical to Controlled.
2. Real-Time Sensitivity Sliders
Enables administrative officers to drag weight sliders (DO, BOD, pH) to simulate changing environmental priorities and re-rank ghats in 0.1 seconds.
3. 100% Traceability & Auditability
Every test links directly to its source annual MPPCB PDF report and exact page number, ensuring decisions are legally defensible in court/NGT.
4. Dynamic Ingestion & New Kund Onboarding
Field inspectors can upload batch multi-parameter Excel/CSV sheets or onboard newly constructed containment kunds with instant automatic re-ranking.

## Slide 4
BHOPAL IMPACT LAB 2026 · TRACK 2
System Architecture & Production Tech Stack
Backend Core
Python 3.10+ Flask Web Server SQLite Zero-Config DB REST API Endpoints
Analytics Engine
Pandas & NumPy MCDA Risk Calculator CPCB Class B Rules Automated YoY Deltas
Frontend & GIS
TailwindCSS & Jinja2 Chart.js Trends Leaflet.js GIS Map Bilingual Switcher
Zero-Config DevOps
Windows 1-Click Launcher run.bat automated venv 7-Step Self Diagnostics test_system.py suite

## Slide 5
BHOPAL IMPACT LAB 2026 · TRACK 2
Bhopal Ghat Priority Ranking & Scientific Findings
#1 Bairagarh (Sant Hirdaram) kund [Score: 69.7 | CRITICAL] — DO hit 0.0 mg/l 4 times; 100% BOD violations; stagnant mineralized kund.
#2 Shahpura lake ghat [Score: 26.6 | HIGH] — 100% BOD violations (18/18 tests); DO fell to 2.5 mg/l in Durga 2025.
#3 Malikhedi kund [Score: 23.5 | HIGH] — Post-immersion organic surge (BOD jumped 1.6 -> 16.8 mg/l in 2023).
#4 Rani Kamlapati / Kamla Park [Score: 20.0 | HIGH] — Chronically polluted Lower Lake; DO stayed at ~2.5 mg/l in Durga 2025.
#5 Hathaikheda dam / kund [Score: 19.1 | MODERATE] — Extreme BOD surge (22.0 mg/l); alkaline pH 8.92; dam reservoir.
#6 Khatlapura ghat [Score: 17.0 | MODERATE] — Baseline Lower Lake pollution; metal & conductivity spike in Ganesh 2024.
#7 Prempura ghat [Score: 6.3 | LOW] — Consistently the cleanest natural lake ghat; lowest median BOD (3.2 mg/l).

## Slide 6
BHOPAL IMPACT LAB 2026 · TRACK 2
100% Dynamic Architecture: Ingestion to Instant Re-ranking
Multi-Parameter Bulk Ingestion
Upload batch CSV or Excel sheets (.xlsx) covering all 13 parameters in a single file. Supports Long and Wide formats with smart context overrides.
Dynamic Ghat Onboarding
Register newly constructed artificial kunds with GPS coordinates. The system automatically creates a dedicated deep-dive trends page with default banners.
Instant Recalculation
Every newly entered sample or uploaded sheet automatically triggers the MCDA engine, recalculates scores, and re-sorts priority rankings in < 1 second.

## Slide 7
BHOPAL IMPACT LAB 2026 · TRACK 2
Core Innovations & Unique Selling Propositions
1. Judicial Auditability (100% Traceability)
No black-box hallucinations. Clicking any test reading opens the official MPPCB annual technical report at the exact page number, ready for court scrutiny.
2. Interactive Administrative Agency
Municipal engineers are not locked into static outputs; dynamic sliders empower real-time adjustment of DO, BOD, and pH priorities.
3. Bilingual Decision Memo
A forwardable bilingual executive memo formatted for WhatsApp/Email sharing or 1-click administrative printing for senior decision-makers.
4. Grounded Conversational AI
A context-grounded bilingual assistant answering complex queries strictly from MPPCB records with phonetic Hinglish matching.

## Slide 8
BHOPAL IMPACT LAB 2026 · TRACK 2
Structured 3-Minute Live Demonstration Flow
Step 1: The Problem (0:00 - 0:45)
Launch localhost:5000 via run.bat. Highlight the 4 KPI cards: 4 zero DO readings at Bairagarh and 89.3% statewide BOD organic pollution.
Step 2: Dynamic Sliders (0:45 - 1:15)
Drag DO slider from 50% to 70%. Show how rankings and Chart.js bar chart re-order live in 0.1 seconds based on MCDA calculations.
Step 3: Deep-Dive & Traceability (1:15 - 2:00)
Open 'View Trends' on Bairagarh. Filter historical readings by year/festival. Click 'Page 28 PDF' to open the original scanned MPPCB document.
Step 4: Dynamic Bulk Ingestion (2:00 - 2:30)
Open 'Import Water Quality Data' modal. Upload multi-parameter spreadsheet and demonstrate automated ranking recalculation.
Step 5: Bilingual AI Assistant (2:30 - 3:00)
Ask chatbot: 'bairagadh ka pani kaisa hai?' Show instant grounded response with verified MPPCB citations.

## Slide 9
BHOPAL IMPACT LAB 2026 · TRACK 2
Empowering Bhopal's Water Heritage
Operational Ready for 20 October 2026 Durga Visarjan
• 100% Open Source: Offered to Government of Madhya Pradesh & MPSeDC. • Zero API Dependencies: Operates entirely locally with high reliability. • Extensible Blueprint: Architecture ready for 100+ immersion sites across MP. Team NeerRakshak: Anoop Shukla (anoopshuklanew00@gmail.com) GitHub: https://github.com/AnoopShukla-ProjectWorld/claude-community-bhopal